## Slide 1: Networking
Marquette University, Fall 2021

## Slide 2: Introduction
https://www.youtube.com/watch?v=2GmLgoQBzUo

## Slide 3: Data Communication
Exchange of information between two entities
  Properties
    Delivery
    Accuracy
    Timeliness
    Jitter

## Slide 4: Data Communications Components
A message has a sender and a receiver
It uses a transmission medium
The transmission follows several protocols

## Slide 5: Data Communication Components
Message
Sender
Receiver
Transmission Medium
Protocol: A set of rules

## Slide 6: Data Representation
Information comes in different forms
Various formats for digital data
  Text: Unicode, ASCII, Latin-1, utf-8
  Numbers: base 1, base 2, IEEE floating point format
  Images:
    Resolution determines number of pixels
    Each pixel contains various scales (e.g. b for color)
  Audio
  Video

## Slide 7: Data Flow Types
Simplex mode:
  Communication is one-directional
Half-duplex:
  Communication is one-directional for a time, then goes in the other direction
Full-duplex:
  Communication is bidirectional

## Slide 8: Networks
Interconnection of a set of devices capable of communication
  Hosts (end-points) vs. Connecting Devices (e.g. routers)
Criteria
  Performance
    Throughput
    Delay
  Reliability
  Security

## Slide 9: Physical Structures
Point-to-point links
  Dedicated link between two devices
Multi-point links:
  More than two devices share a link
    E.g. Token Rings (IBM / IEEE 802.5)
Physical Topology
  Two or more devices connect to a link
  Two or more links form a topology

## Slide 10: Simple Network Topologies

## Slide 11: Network Types
Networks are limited by
  throughput
  delay (i.e. distance)
    Local Area Networks
    Wide Area Networks
    Internets

## Slide 12: Network Types
LAN: Local Area Network
  bus
  switched

## Slide 13: Network Types
WAN: Wide Area Network
  Point-to-point (two ends)
  Switched WAN (used as backbone for Internet)

## Slide 14: Network Types
Internets (with a small i) aka. internetworks
  Connects several LANs or WANs
  Circuit switched
  Packet switched

## Slide 15: Network Types
Data communication
  Data are bursty
  No causality
  More bandwidth = faster transmission
  Data loss very bad
Circuits
  Data are streamed
  Signals are causal
  Signal has finite bandwidth
  Some signal loss tolerable

## Slide 16: Heterogeneous Network

## Slide 17: Switching
Switched networks (e.g. internet)
  Switch forwards data from one network to another
  Circuit switched networks
    Dedicated network (circuit) is always available between two systems
  Packet switched networks
    Instead of continuous connections
    Use blocks of data: packet

## Slide 18: Internet
Internet (capital I)
  Consists of thousands of interconnected networks
  Has several backbones
    Owned by Sprint, Verizon, ATT, NTT, ...
    Connected via peering points
  Has a larger number of provider networks
    which use the backbones for a fee
    connected to several backbones and possible other provider networks
  Customer networks use the services of these Internet Service Providers

## Slide 19: Internet Standards
Internet draft: Working document with no status and 6 month expiration date
Request for Comment is next stage:
  Proposed Standard
  Draft Standard (needs at least two interoperable implementations)
  Internet Standard: adhered by all
  Historic: never passed or superseded
  Experimental
  Informational

## Slide 20: Internet Standards
RFC:
  Required (must be implemented) e.g. TCP, IP
  Recommended e.g. FTP, TELNET
  Elective
  Limited Use
  Not recommended (only for historic RFC)

## Slide 21: Internet Administration
ISOC: Internet Society
  formed 1992 to provide support for Internet standard process
IAB: Internet Architecture Board
  technical advisor to ISOC using
      IETF: Internet Engineering Task Force
      IERF Internet Research Task Force
  Manages RFCs
  External Liaison to other standards organizations

## Slide 22: Protocol Layering

## Slide 23: Layered Architecture
Layering was invented to deal with complexity of software development
  THE Operating System
In Networking there are additional motivations
  Plethora of underlying technologies and needs
  Networking devices often do not need full functionality

## Slide 24: Layered Architecture
Principles of protocol layering for networking
  Bidirectional communication implies that each layer needs to perform two opposite task, one in each direction
      Listen
      Talk
  Objects exchanged under each layer need to be identical

## Slide 25: Layered Architecture
TCP/IP stack
  Application layer
  Transport layer
  Network layer
  Physical layer

## Slide 26: Layered Architecture

## Slide 27: Layered Architectures
Messages
Segments / User datagrams
Datagrams
Frames
Bits

## Slide 28: Physical Layer
Carries individual bits in a frame across a link
  Devices are connected by a transmission medium
    Media have different characteristics
  Bits are transformed into a signal

## Slide 29: Data Link Layer
Takes datagram and moves it as a frame across the link
Different link layer protocols may provide different services
  Error detection
  Error correction

## Slide 30: Network Layer
Responsible for creating a connection between source and destination (end-to-end connection)
IP - Internet Protocol
  Connectionless
  no flow control
  no error control
  no congestion control
Auxiliary protocols: Internet Control Message Protocol, Internet Group Management Protocol, Dynamic Host Configuration Protocol, Address Resolution Protocol

## Slide 31: Transport Layer
Transmission Control Protocol
  Provides flow control, error control, congestion control
User Datagram Protocol
  Connectionless without flow, error, and congestion control
Stream Control Transmission Protocol
  Designed for multimedia

## Slide 32: Application Layer
Two applications exchange messages
  HTTP between browser and web-server
  FTP
  Telnet
  SSH
  SNMP
  DNS
  IGMP

## Slide 33: Encapsulation
Each layer adds a header (which could also be a tail or both) to a message
For receiving, each layer strips its header

## Slide 34: OSI Model
Open Systems Interconnection (OSI) Model
  After TCP/IP model (late 70s)
  Established by International Organization of Standardization (ISO)
  Came to late to change TCP/IP stack
  Never defined some layers completely

## Slide 35: OSI vs TCP/IP

## Slide 36: Internet Standards
Proposed Standard
Draft Standard (becomes RFC)
  (after >1 successful interoperable implementations)
Internet Standard
Historic RFC
  superseded or never became an Internet standard
Experimental
Informational

## Slide 37: Internet Administration